## Slide 1: Introduction to IPSO Smart Objects
Jaime Jiménez, Ericsson Research, IPSO Smart Objects co-chair.
jaime.jimenez@ericsson.com
June 15th, 2015

## Slide 2: IPSO Smart Objects
Developed by IP for Smart Objects (IPSO) Alliance in the Smart Objects Working Group.
Work exclusively on semantic Interoperability across IoT devices and applications.
Based on LWM2M Object Model.
Reusable Object IDs and Resource IDs.
Transport Protocol Independent (CoAP, LWM2M, MQTT, HTTP, XMPP…) if it supports addressing, content formats and data types.
Encoding Independent (JSON, TLV, SenML…)
Basic Objects represent simple sensors and actuators.
IPSO Smart Object Guidelines: Starter Pack published on 2014 (Expansion Pack upcoming).
  http://www.ipso-alliance.org/technical-information/ipso-guidelines
Tested over CoAP and LWM2M during IPSO Interoperability test on May 2015 (ARM, Ericsson, Intel, SICS, Yanzi, TUT …) .
Notes: Since we have only few slides and little time, I will focus on being pragmatic and on the content and message of this presentation.
IP for Smart Objects is an Alliance of several companies, you can find that information on the IPSO Alliance Website. IPSO has few committees, among those the IPSO Smart Objects Committee where we define Smart Objects.
The overall goal is for semantic interoperability btw devices (sensors and actuators) and the applications that use them. We are creating a standard set of semantics that can be used to provide plug and play interoperability btw devices and applications.
We have taken the LWM2M Object model almost as it is. LWM2M Objects are used for management of devices, they provide a clear URI format for addressing those management objects, as well as access control, instantiation and resources.
In IPSO we extend that model with the concept of reusable resources. The goal is that if you have some specific sensor, you can take one of the existing IPSO Objects and use it as it is or take its resources and extend it to suit your particular device characteristics.
We have designed IPSO Objects to be transport protocol independent. It obviously supports CoAP as it is based on LWM2M objects, but people have used them with MQTT or HTTP as well. So you can basically send the object data over as long as you support the basic data types and content formats.
Also for serialization it will depend on the protocol, can be TLV, JSON, plain text . For example we have successfully done interop tests with TLV and plaintext.
We have already released a basic set of smart objects last year, with some very common sensors and actuator templates, you can go and have a look at the website or you can let us know if you are interested on using them or give feedback and so on.
We also have tested it between the partners in IPSO few weeks ago. Each brought their own implementation of IPSO objects, we used CoAP LWM2M for the application layer and tested it over an IPv6 network

## Slide 3: Roadmap
☐ UPnP harmonization – from SOAP to REST.
☐ BLE/ZigBee harmonization.
✔ Draft Smart Object Data Model Design Guide @done (15-03-30)
✔ Draft Smart Object Expansion Pack for Basic Objects @done (15-04-30)
✔ Set up test servers for IPSO objects (LWM2M + TLV payload) @done (15-06-15)
☐ Draft Domain Specific Objects reference designs @due (mid 2015)
☐ Publish Smart Object Data Model Design Guided @due(15-07-31)
☐ Publish Smart Object Expansion Pack for Basic objects @due(15-07-31)
☐ Publish Smart Object Expansion Pack for Composite Objects @due(15-07-31)
☐ Publish Smart Object Expansion Pack for Reference Devices @due(15-07-31)
☐ IETF 93 – Bits and Bites @due(15-09-1)
Notes: At the moment we are working with other standards in order to come together to a common data model. For example with UPnP we are currently trying to harmonize the large amount of resuorce descriptions in UPnP with the IPSO Objects. Some of the challenges here is that UPnP uses more of a SOAP approach with its Message Exchange Pattenrs than a REST-based one.
Interworking with TR69, ZigBee, BLE and how to harmonize them so that there is one set.
We have also some deadlines, this list is taken from our item activity document. So basically we are setting up some test servers for continuous testing of Smart Objects, in this case over IPv6 and LWM2M.
We are also working on various expansion packs, like the domain specific objects (GW Objects, Home Appliances, etc)
We have to produce a standalone schema on how to construct the objects and how clients and servers are supposed to use them.
We are also working on Composite objects, by using a new data type that represents a link. So that we will have resources that do not only map to a specific resource, rather it will be more like the web and we will use linking instead.
Also we will have a session in November in the IETF bits and bites. There we will show how objects work, some examples, how to create them and so on.

## Slide 4: Next Steps
Activities
  Working with Smart Objects: Expansion Pack, Composite Objects, Linked Objects.
  Collaboration with other IoT Interest Groups like UPnP, IIC, OIC.
  Work on related Standards organizations: IETF CoRE - CoAP, OMA DM - LWM2M.
  Prototyping and testing (IETF 93, Bits and Bites, 2nd IPSO Interop, …)
Focus Area
  IPSO Smart Objects are meant to be very generic.
  Any vendor can use them for their specific area by creating their own Objects by reusing generic resources and add their own.
Absolutely necessary for IoT
  Harmonization and mapping between different data models & standards.
  Use of standards for Application Level interoperability btw devices and applications vs propietary solutions.