## Slide 1: Introduction to IPSO Smart Objects
Jaime Jiménez, Ericsson Research, IPSO Smart Objects co-chair.
June 15th, 2015

## Slide 2: Problems to solve in IoT
Interoperability
  Software’s interaction with physical resources.
  Device independence from software management and vendors.
  Discovery, Management, Reporting, Security, Authorization.
Scalability
  Billions of devices, users, connections…
  Billions of interactions.
Reusability and modularity
  Software, networks, protocols, data models.
  In a vertical segment, across vendors.
  Across diverse vertical segments.
Permissionless Innovation
  Enable anyone to participate and innovate.

## Slide 3: IPSO Smart Objects
Developed by IP for Smart Objects (IPSO) Alliance in the Smart Objects Working Group.
Work exclusively on semantic Interoperability across IoT devices and applications.
Based on LWM2M Object Model.
Reusable Object IDs and Resource IDs.
Transport Protocol Independent (CoAP, LWM2M, MQTT, HTTP…) if support addressing, content formats and data types.
Encoding Independent (JSON, TLV, SenML…)
Basic Objects represent simple sensors and actuators.
Basic Starter Pack published on 2014 (Expansion Pack upcoming).
Tested over CoAP and LWM2M during IPSO Interoperability test on May 2015 (ARM, Ericsson, Intel, SICS, Yanzi, TUT …) .

## Slide 4: The Web in constrained devices
IPv4 / IPv6
IPSO Objects
Applications
6LowPAN
HTTP
CoAP
LWM2M
Web Server
Data Models
Application
API / Services
Routing
802.15.4
MCU
Wifi, Ethernet, LTE, …
MPU
Application Protocol
HW Network
Hardware

## Slide 5: IPSO Smart Object Structure
Reusable resource and object IDs
  Common definitions for concepts
  Map to semantic terms e.g. temperature, currentValue
  IDs are registered with the OMNA
Usable in different transport protocols that support
  URI Addressing
    (…/home/weather/3303/0/5700)
  Data Types
  Content Formats
  RWX Operations
3303/0/5700
Object ID, defines object type
Object Instance, one or more
Resource ID, defines resource type

## Slide 6: Example: IPSO Humidity Sensor
Resource Name | Resource ID | Access Type | Multiple Instances? | Mandatory | Type | Range or Enumeration | Units | Descriptions
Sensor Value | 5700 | R | No | Mandatory | Float |  |  | Last or Current Measured Value from the Sensor
Units | 5701 | R | No | Optional | String |  |  | Measurement Units Definition e.g. “Cel” for Temperature in Celsius.
Min Measured Value | 5601 | R | No | Optional | Float | Same as Measured Value | Same as Measured Value | The minimum value measured by the sensor since power ON or reset
Max Measured Value | 5602 | R | No | Optional | Float | Same as Measured Value | Same as Measured Value | The maximum value measured by the sensor since power ON or reset
Min Range Value | 5603 | R | No | Optional | Float | Same as Measured Value | Same as Measured Value | The minimum value that can be measured by the sensor
Max Range Value | 5604 | R | No | Optional | Float | Same as Measured Value | Same as Measured Value | The maximum value that can be measured by the sensor
Reset Min and Max Measured Values | 5605 | E | No | Optional | Opaque |  |  | Reset the Min and Max Measured Values to Current Value
Object | Object ID | Object URN | Multiple Instances? | Description
IPSO Humidity | 3304 | urn:oma:lwm2m:ext:3304 | Yes | Relative humidity sensor, example units = %

## Slide 7: Roadmap
☐ UPnP harmonization – from SOAP to REST.
☐ BLE/ZigBee harmonization.
✔ Draft Smart Object Data Model Design Guide @done (15-03-30)
✔ Draft Smart Object Expansion Pack for Basic Objects @done (15-04-30)
✔ Set up test servers for IPSO objects (LWM2M + TLV payload) @done (15-06-15)
☐ Draft Domain Specific Objects reference designs @due (mid 2015)
☐ Publish Smart Object Data Model Design Guided @due(15-07-31)
☐ Publish Smart Object Expansion Pack for Basic objects @due(15-07-31)
☐ Publish Smart Object Expansion Pack for Composite Objects @due(15-07-31)
☐ Publish Smart Object Expansion Pack for Reference Devices @due(15-07-31)
☐ IETF 93 – Bits and Bites @due(15-09-1)

## Slide 8: Next Steps
Activities
  Working with Smart Objects: Expansion Pack, Composite Objects, Linked Objects.
  Collaboration with other IoT Interest Groups like UPnP, IIC, OIC.
  Work on related Standards organizations: IETF CoRE - CoAP, OMA DM - LWM2M.
  Prototyping and testing (IETF 93, Bits and Bites, 2nd IPSO Interop, …)
Focus Area
  IPSO Smart Objects are meant to be very generic.
  Any vendor can use them for their specific area by creating their own Objects by reusing generic resources and add their own.
Absolutely necessary for IoT
  Harmonization and mapping between different data models & standards.
  Use of standards for Application Level interoperability btw devices and applications vs propietary solutions.